## Slide 1: Data Collection & Pre-processing

## Slide 2: Introduction: Data source design
UAV data is “complex” because it is multi-modal (variety), high-rate & heavy (volume/velocity), and noisy/irregular
Time sync, coordinate consistency, calibration, denoising, and schema normalization before any Machine Learning algorithms is applied.
Turning messy, multi-modal inputs (telemetry, IMU, camera, LiDAR, surveys, APIs) into well-defined tables with clear schemas, units, IDs, and timelines.

## Slide 3: Core principles for UAV Data
Attributes (columns) you need to create
flight (one mission) ↔ telemetry (time series) ↔ events (mode changes)
External/context: weather_snapshot, airspace_polygon, geofence_rule, survey_annotation
Payload refs: image_asset, lidar_asset (store metadata + path, not the binary itself)
Time & synchronization
Use UTC everywhere; store as datetime64[ns, UTC].
Keep raw sensor timestamps and a unified timeline after resampling (e.g., 10 Hz).
Coordinates & units
Positions: WGS84 (lat/long), plus a local ENU frame
WGS84: address on Earth’s globe, and ENU: local X–Y–Z grid around you.
Altitude: declare reference (AGL or MSL) and units (meters).
Use SI units: speed_ms, altitude_m, accel_mps2.

## Slide 4: Core principles for UAV Data
d) Identifiers & naming
flight_id (UUID), uav_id, segment_id (optional per takeoff–landing).
Consistent snake_case, unit-suffixed names (e.g., altitude_m, speed_ms).
e) Storage tiers & formats
Bronze (raw JSON/CSV as collected) → Silver (cleaned, typed, normalized) → Gold (features/labels).
f) Streaming vs batch
Telemetry/health → streaming (WebSocket/UDP) into small chunks.
Photos/LiDAR → batch uploads with metadata rows.

## Slide 5: Surveys
What you get: Pilot notes, checklists, field labels, geotagged photos, target presence/condition ratings.
Why complex: Human-entered data → typos, inconsistent scales, missing timestamps; subjective labels.
Typical problems: Free-text ambiguity, mismatched identifiers vs telemetry, sparse sampling.

## Slide 6: Flight telemetry APIs
What you get: MAVLink/SDK streams: position, attitude, motor RPM, battery, flight mode, health; 5–50 Hz per stream.
Why complex: Multiple message types at different rates, occasional packet loss, firmware-dependent fields, mixed units.
Typical problems: Out-of-order packets, duplicate messages, mode changes mid-mission, missing fields.
Preprocessing tips:
  Parse to a typed schema (e.g., one tidy table per signal family).
  De-duplicate, sort by timestamp, resample to common rate.
  Validate ranges (battery 0–100, attitudes in ±π, etc.) and flag anomalies.

## Slide 7: 1) Airspace / NOTAM / TFR APIs
Keep flights legal and safe by checking permanent rules and temporary restrictions.
Critical because airspace status can change hours or minutes before launch (VIP movements, wildfire TFRs, parachute ops). Without this check, you risk regulatory violations, fines, or loss of aircraft.
Provide polygons with effective start/end times, altitude floors/ceilings, required authorizations, contact details.
Use in workflow:
Pre-flight: fetch current notices for your planned area/altitude.
In-flight: monitor for new TFRs and trigger re-routes or RTL.
NOTAM → Notice to Air Missions
TFR = a kind of notice about temporary no-fly zones

## Slide 8: 2) Geofencing APIs
Enforce where a drone may (or may not) fly—fixed critical zones (airports, prisons, power plants) and your own operational bubbles.
Prevents airspace incursions and ground risk (e.g., crowds). It’s your last line of defense if GPS drifts or wind pushes you off track.
Provide No-fly and authorization-required polygons, buffers, altitude caps, rationale codes.
Use in workflow:
Pre-flight: plan a corridor that avoids restricted areas.
In-flight: continuous point-in-polygon checks; if inside, slow/stop/RTL.

## Slide 9: 3) UTM (Uncrewed Traffic Management) APIs
Deconfliction and accountability when many drones (and crewed traffic) share airspace.
Critical because it enables flight intent submission, airspace authorization, conformance monitoring, and detect-and-avoid advisories via standardized, provider-to-provider messaging.
Provide flight plan acceptance/constraints, strategic deconfliction results, live advisories, Remote ID/telemetry exchange policies.
Use in workflow:
Pre-flight: submit plan → receive authorization/time window/altitude limits.
In-flight: stream conformance; if you deviate, get alerts and new constraints. Design tip: UTM is event-driven—use WebSockets/pub-sub; REST is for configuration/history.

## Slide 10: 4) Weather APIs
Quantify air risk and energy budget (wind, gusts, rain, density altitude) for go/no-go, route choice, and battery reserves.
Critical because wind aloft and gusts, not surface wind, often determine mission success and link reliability. Micro-weather drives energy consumption, landing distance, and GPS multipath risk in urban canyons.
Provide time-series by height (wind/direction/gust), precipitation, visibility, temperature/pressure (for density altitude), sometimes thunderstorm risk.
Use in workflow:
Pre-flight: compute expected Wh consumption vs waypoints and reserves; set safe speed/altitude.
In-flight: update ETA, battery margin; trigger contingency landing if gusts exceed thresholds.

## Slide 11: Sensors: GPS (GNSS)
Latitude/longitude/altitude, velocity, fix quality, dilution of precision; 1–10 Hz (RTK up to 20 Hz).
Why complex: Multipath/reflections near buildings, temporary outages, jumps between fixes, different altitude references (MSL vs ellipsoid).
Typical problems: Missing points, sudden position “jumps”, inconsistent time bases.
Preprocessing tips:
  Smooth with a low-pass or Savitzky–Golay filter for small jitter.
  Convert to a local frame (ENU) for ML/controls.
  Interpolate to a common timeline before sensor fusion.

## Slide 12: Sensors: IMU (accelerometer + gyroscope [+ magnetometer])
Accelerometer Measures linear acceleration (how fast you’re speeding up/down, left/right, up/down).
Gyroscope Measures angular velocity (how fast you’re rotating around each axis: roll, pitch, yaw).
Magnetometer Measures the Earth’s magnetic field → works like a digital compass.
Why complex: High-rate, noisy and biased signals; gyros drift; hard real-time sync with other sensors.
Typical problems: Bias/scale errors, integration drift, clock drift across devices.
Preprocessing tips:
  Bias estimation on still segments; high-pass/low-pass filtering.
  Fuse with GPS/camera via EKF/UKF or factor graphs to bound drift.
  Keep everything in consistent frames (body ↔ world) using quaternions.
IMU = Inertial Measurement Unit

## Slide 13: Sensors: Camera
What you get: High-bandwidth images/video (e.g., 4K@30 fps), often rolling shutter.
Why complex: Huge volume, lighting changes, motion blur, lens distortion; timestamps must align with IMU for VIO/SLAM.
Typical problems: Dropped frames, exposure variation, distortion, misalignment with IMU/GPS.
Preprocessing tips:
  Undistort (known intrinsics), stabilize exposure/white balance.
  Synchronize with IMU (hardware triggers preferred).
  Downsample/tiling; extract features (ORB/SIFT) if storage/bandwidth matters.

## Slide 14: Sensors: LiDAR
Provides Point clouds (10⁵–10⁶ pts/frame), intensity, timestamps.
Complex because data is Very large, uneven density, moving-object artifacts, weather effects (rain/fog), reflectivity biases.
Typical problems: Outliers, multipath returns, mis-calibrated extrinsics to body/camera.
Preprocessing tips:
Outlier removal (statistical/RANSAC), voxel downsampling.
Ground segmentation; normal estimation.
Rigid alignment (ICP/NDT) to build maps; careful extrinsic calibration to camera/IMU.